## Slide 1: OneWire Brief
Dave Campbell
Enchanted Engineering
Sunday, November 6, 2022

## Slide 2: Scope
Capture definition of Dallas Semiconductor operation and design.
Identify personal experiences and use.
Dallas Semi/Maxim App Notes and References:
  DS Tech Brief 1: MicroLAN Design Guide (By Dan Awtrey, OneWire Developer)
  US5210846 One Wire Patent
  AP937: iButton Manual (OneWire Standard)
  AN126: 1-Wire Communication Through Software
  AN148: Guidelines for Reliable 1-Wire Networks
  AN187: 1-Wire Search Algorithm
  AN27: Understanding 1-Wire CRC
  AN214: 1-Wire Using a UART
  Datasheets of various OneWire device
  How to use 1-Wire bus in Linux (http://WWW.SEAHU.CZ)

## Slide 3: OneWire in a Nutshell
Simple single Master, multiple Slave OneWire (+ ground + optional power) low speed (open drain, wired-OR) serial sensor/data network protocol defined by and proprietary to Dallas Semiconductor, now Maxim.
  Very tolerant asynchronous PWM timing protocol (-50% /+100%  ½X / 2X).
  Bus initialized (reset) before all messages (No bus lockup like I2C).
  Very low power (1 uA) per slave allows ~1000 devices/net.
  Controlled edges means low EMI and use of bare wire up to 1000 ft — no transmission line.

## Slide 4: OneWire Master
Many implementations…
  DS2480 RS232 (USB) to OneWire interface.
  Other devices for I2C.
Maxim offers a VHDL/Verilog synthesizable OneWire Master for free.
  Verilog and VHDL.
Easily implemented by port pin of microprocessor or FPGA.
  Royalty free Master.
Trades between software and hardware complexity.

## Slide 5: OneWire Slave Devices
Unique 64-bit ID for all devices: family code [8 bit], serial number [48 bits], and CRC [8 bits].
Powerful dynamic self-discovery protocol (b-tree) for all Slave devices.
Parasitic bus-powered devices (5V, optional independent supply).
Embedded functions, such as keyless entry systems, marketed as iButtons (long before iPhones, iPods, iPads, etc)

## Slide 6: Commerical Slave Devices
Commercial devices encompass a large number of functions including …
  Temperature sensing (DS18B20, DS28EA00).
  Thermostat control (i.e. temperature sensing with limit detection and discrete output such as DS2422).
  Discrete switches (DS2408, DS2413).
  Real Time Clock and calendar timekeeping.
  Battery monitoring (DS2438).
  A/D conversion (DS2450).
  Counting (DS2423).
  ID serial numbers (DS2401, DS2411).
  EEPROM and RAM, with and without encryption (DS28E01-100).

## Slide 7: OneWire Slave Emulation
User can emulated slave devices by both software and hardware means.
  Although patents have expired, Maxim has sued others introducing products to market.
  Patent law allows anyone to use patented designs for personal use, as long as it does not impair the patent holders earnings.
Bus timing places very tight restrictions on software responses.

## Slide 8: Bus Bit Protocol and Levels
Communication by pulse width modulation of “bus slots”.
All “bits” initiated by Master, relieving Slave of global time keeping and allowing control of all edges* by Master only.
  Slaves require no special driver requirements; must sink > 2 mA.
  Only Master requires slew rate control for high-to-low transition.
  Normally, low-to-high transition controlled by pull up and bus load capacitance.
  Tolerant to long rise and fall times (>1 uS) for low EMI.
  *Exception is the presence pulse initiated by slave. Workaround s exists to override the Slave initiated Presence Pulse by simply having the Master issue a preemptive presence pulse before any slave (think of the Master as being the fastest Slave) or to add slew control to Slaves as in newer devices or add parasitic slave series R (<100) and bus shunt C. However, presence pulse generally never causes issues as protocol specifies a long recovery time following presence pulse.
Bus Levels
  Defined originally as 5V bus voltage, but most devices work to 3V.
  TTL logic levels (with hysteresis, VIL~0.8V, VIH~2.4V).
  Some older memories require 12V programming voltage, but external to bus.

## Slide 9: Bus Timing Definitions
Philosophically speaking, the OneWire protocol allocates maximum tolerance to the Slave devices and forces a flexible Master implementation to compensate. This makes Slaves cheap and assures a high degree of operability without difficult specs. (Realize OneWire development began when processes had much greater tolerances than today.)
Dallas Semiconductor (DS), original developer, defines all timing in terms of a nominal Master bus time slot of 60uS, maximum 120 uS, minimum 30uS. This leads to some confusion scaling other timing.
Easier to consider all timing relative to a nominal Slave period, tp, of 30uS, the point in time that the Slave strobes the bus state (i.e. Slave read) and the minimum amount of time that the Slave guarantees its response to the Master (i.e. Slave write), as assumed in following diagrams.
  Then consider specs apply for 15uS<tp<60uS (1/2X to 2X tolerance).
  All DS timing specs are line-to-line having no margin and do not account for rise and fall times. If Slaves encompassed the full tolerance, there would be bus errors.
  In practice, Slaves tend to be much more nominal +/-15%.

## Slide 10: Bus Master Timing Rules
The Master initiates all timing.
To write a “1”, the master drives the bus low <1 minimum slave time period (including rise time); <1 tPMIN, thus <15 uS.
  Recommend tW1=3-5 us to allow longer bus charge recovery.
To write a “0”, requires driving the bus low for at least 1 tPMAX=60us, and no more than 8 tPMIN = 120us.
  Recommend tW0 = 60-75us.
For read, the master must sample the bus <1 tPMIN, thus <15 uS.
  Recommend tRD=12 uS.
  Reading is no different than writing a 1, which the slave modulates.
  All reads require a write (1) operation for each bit read, thus bus data can be thought of as always being bidirectional, 1 bit sent = 1 bit received.
Bus must return high for at least 1 uS before next bit.
  Recommended recovery time, tREC = 10-15us.
  Writing a series of 0’s with insufficient recovery time will discharge the bus (and internal parasitic power storage), resulting in errors.

## Slide 11: Bus Slave Timing Rules
A slave responses to the master generated falling edge.
For a read operation, the slave samples at end of 1 Slave period, 15uS< tP <60uS.
  Target 30 uS.
To write a “1”, the slave takes no action. (i.e. timing completely defined by Master).
To write a “0”, the slave holds bus low for 1 slave time period, 15uS<tP<60uS (i.e. longer than the Master tRD sample time, ~12-15uS).
  Target 30 uS.

## Slide 12: Bus Timing Specs

## Slide 13: Bus Reset Timing
A bus reset pulse is issued anytime the Master wishes to initialize the bus, normally before all communications.
The Master pulls the bus low for 16 Slave timing periods.
  Target 30 uS * 16 = 480uS.
  Must be less than 960uS for interrupt compatibility (i.e. < 16 tpmax =64 tpmin).
  [tRST = 16tp = 32tPMIN = 8 tPMAX= 480uS] < [tINT = 32tp = 64tpmin = 16 tpmax = 960uS]
  Since controlled by stable Master timing, assumed not dependent on Slave timing.
The Master must wait 16 Slave timing periods after a reset before initiating follow on communications to allow for bus recovery and recharging of parasitic supply capacitors, as well as presence detection.

## Slide 14: Bus Presence Pulse Timing
Following a reset, Slaves issue a “presence pulse” to acknowledge their listening state on the bus.
  No pulse means no devices present on the bus (or a stuck-at fault).
  Slave timing defines the presence pulse …
    The leading (falling edge) governed by the fastest Slave to respond after the reset pulse, 1 tpMIN.
    A presence pulse is specified as 4 tP in width.
    The trailing (rising) edge governed by the slowest Slave response after the leading edge, 4 tPMAX.
    Thus, by measuring the presence pulse relative to the reset pulse, the Master can determine the range of timing for Slave devices, allowing the Master to optimize timing, although this is not normally necessary or implemented.
Master presence sense must occur between 1 tpmax (60us) and 5 tpmin (75us).
  Target 60 uS.
Since the leading edge is not controlled by the Master for this exception case, fall time is may not be controlled.
  Alternately, the Master can initiate an “early” presence pulse to avoid this, but this prohibits presence detection. This could be a configurable condition to minimize EMI, but also allow characterization on demand; however, as noted previously generally not a problem..

## Slide 15: Bus Reset and Presence Timing
NOTE: SLAVE TIMING NOT SYNCHRONOUS WITH MASTER AS APPEARS ABOVE

## Slide 16: Basic Message Protocol
The OneWire protocol implements robust serial communications with error checking.
All messages begin with a RESET operation, presence detect, followed by a ROM command.
All parts addressed by 64-bit unique ID** also referred to as the ROM code after the ROM command.
  8 bit family code (LSB).
  48 bit unique serial number.
  8 bit CRC-8 check byte (MSB).
Other Commands/Data follow as defined for the specific part.
** STRICKLY SPEAKING THE SKIPROM COMMAND DOES NOT SEND THE 64-BIT ADDRESS, SEE ROM COMMAND DESCRIPTION FOR DETAILS.

## Slide 17: Required ROM Functions
The internal 64-bit ROM code represents a device’s serial number and functions as a unique bus address for the device.
Required ROM Commands include…
  Skip ROM [0xCC]
    Assumes address match. Only works for a single device on the bus. Useful for device test.
    NO serial number sent for skip ROM command.
  Read ROM [0x33]
    Slave returns internal ROM code. Only works for a single device on the bus. Useful for device test.
    Master reads only.
  Match ROM [0x55]
    Addresses only the single Slave device whose ROM code matches the value sent by the Master. Basic mechanism to deselect all other device communications. Essentially only command used for operations.
  Search ROM [0xF0]
    Enables an algorithm for acquiring the ROM value for all devices on a bus in a determinist fashion. Expands ROM value into 3 bit times per bit. See Search Algorithm for details.

## Slide 18: Bit Ordering Gotchas
Always LSB first; however, for convenience device serial numbers generally specified in hex, beginning with the family code (e.g. 3A), ending with the CRC sum, as in … 3A 37 A7 00 00 00 00 95 5A FE 01 AA FF
But the true bit ordering for this device, read right to left (i.e. LSB to MSB), would be FF AA 01 FE 5A 95 00 00 00 00 A7 37 3A or in binary (MSB) 1111 1111 1010 … 0111 0011 1010 (LSB)
Observed on a scope or logic analyzer would be (LSB) 010111001110 … 010111111111 (MSB)
Note: Observed in memory the serial number may appear in either order depending on big endian or little endian architecture.

## Slide 19: CRC Functions
OneWire uses CRC8 for bus address verification.
  Polynomial x8 + x5 + x4 + 1.
  Initial value 0.
  0 for valid check.
OneWire generally uses inverted CRC16 for other data verification., such as memory operations.
  Polynomial x16 + x15 + x2 + 1.
  Initial value 0.
  Inverted when stored.
    Used to prevent valid CRC for stuck at zero bus!
  0xB001 when valid.

## Slide 20: Search Algorithm (Self-discovery)
B-tree-like search algorithm supports deterministic self-discovery of a single device per pass.
Accelerator built in to DS2480 Master controller to relieve host processor.
For each ROM bit, process generates 3 bus slots …
  Time slot 1: ALL Slaves write their ROM bit; Master reads bit.
  Time slot 2: ALL Slaves write complement of their ROM bit; Master reads complement bit.
  Time slot 3: Master writes desired select bit based on the match results of the search algorithm truth table.
    If a conflict exists, this value determines which b-tree branch to take. Algorithm always takes the “zero branch” first.
    Algorithm works from last conflict back until no conflicts occur, indicating last device found.
    All slaves that don’t match Master specified value at current bit position stop listening for the duration, that is until the next reset.
At end of each pass, the algorithm resolves a single serial number.
  Conflict positions indicate remaining “1 branches” to search, which continues from last branch.
  Discovery time ~20 ms per device.
Search Algorithm Truth Table | 
READ | Means
0 1 | All slave addresses have 0 at this bit position.
1 0 | All slave addresses have 1 at this bit position.
0 0 | Conflict: Multiple Slaves with both 1 and 0 values present at this bit position that wire-OR to zero in both slots.
1 1 | No devices present — Error stop search
COMPLEMENT BIT (SECOND)
TRUE BIT (FIRST)

## Slide 21: (Truncated) Search Example

## Slide 22: Search Issues
The search algorithm offers a powerful mechanism to automatically discover a complete OneWire network; however, it can only detect devices on the network, not physically locate them.
  For example, if the network has 2 DS18B20 temperature sensors it will discover their addresses but not which one is which.
  Some newer parts, DS28E04 for example, offer “chainable” discovery to overcome this.
Search is not required for most embedded applications if one predetermines sensors placed in a network (i.e. search/discover at the “factory”).
  This makes more sense when identifying multiple sensors. For example, a (non-volatile) configuration object that defines inside and outside temperature sensors identifying their respective serial numbers and perhaps other configuration parameters.
“i-Button” devices that periodically “touch” the network, require a current search to determine “who” is presently on the network.

## Slide 23: OneWire Overdrive
Optional mode defined by spec to increases bus speed.
In a practical sense, overdrive applies only to small networks and only specific device types.
  Switched by command.
  Roughly a 10X increase in timing.
    Adjustment for minimum low state.
  Dictates faster rise and fall times.
    Higher EMI mode.
    Greater physical bus constraints in terms of length and capacitance.
  Requires flexible or reconfigurable Master timing for pulse widths and delays.
Not all that useful. OneWire is a slow protocol! Reading bits 10X faster has virtually no bandwidth impact when the sensor takes 1 second to convert a single reading.

## Slide 24: OneWire Alarms & Interrupts
Optional, but necessary to fully support functionality of certain parts.
Alarms and interrupts require additional Master intelligence, not needed for most applications (and not usually supported).
Some parts support alarms.
  Handled as conditional MATCH ROM commands.
Some parts support bus interrupts.
  Type 1 Spontaneous Interrupts: Slave immediately pulls the bus low for 64 periods (960-3840 uS). Master must be able to detect this condition.
  Type 2 Delayed Interrupts: Slave extends the Master Reset pulse to 64 periods. Master must be able to detect this condition.
  Both types difficult for Master to handle and can lead to other problems, particularly for parasitic operations.

## Slide 25: My OneWire
My Hardware and Software Conventions (Personal Use and experience)

## Slide 26: My Experience
I’ve been using OneWire networks and devices for over 20 years.
I’ve built multiple networks with dozens of devices; some have been running reliably for more than 15 years.

## Slide 27: Cabling
Dallas Semiconductor demo weather station (c. 1997) used standard phone system RJ14-6 (6P6C) connectors with 2-wire phone cabling for their weather station, which has become a de facto standard, but lacking a formal pin definition and ordering.
I use 4-wire RJ14 (6P4C) and RJ11 (4P4C):
  1: V5 +5V regulated power.
  2: IO 1 wire I/O pin. (de facto, 1-wire weather station)
  3: GND Ground return. (de facto, 1-wire weather station)
  4: V12 Optional unregulated battery, generally 12V.
  Notes:
  CAUTION: Due to library discrepancies for pin ordering/numbering of the RJ-14 connectors, some board layouts inadvertently flipped connector pinouts. This can be “fixed” with the use of a crossover cable, but mis-wiring between the two definitions can lead to bus shorting and potential part damage.
  Power routing for convenience and reference use. Current draw must be limited and low-noise to not interfere with 1-wire communications. Rule of thumb: <<10mA per node, with local bypass.
  This definition allows use of 2-wire cable (pins 2 and 3) and same connectors for parasitic sensors not requiring external power.

## Slide 28: DS2480B – Serial to OneWire I/F
To minimize bus errors:
  Maximize recovery time.
  Extend write-1 low time to 3-5 uS.
Beware non-realtime OS (i.e. Windows, Linux) may lose data particularly after long delay between messages, for example, waiting for DS1820B temperature conversion.
  Data loss observed to be related to serial driver, not 1-wire bus.
  Requires extra data filtering.

## Slide 29: Hardware Interface
I recommend NEVER directly exposing an IC pin to the bus. Use some form of filtering/isolation and ESD protection.
Constant current drive offers improved performance over simple resistive pullup.
  Will support parasitic DS18B20 operation without strong I/O drive if pullup current exceeds 1mA. (Note: may require >2mA for some newer devices.)
  I recommend ~2mA current (<4mA), which provides faster response for heavy capacitive loads.
Local filtering (C~0.5-1nF) at Master provides more uniform bus operation across varying network lengths/loads.
  Also improves ESD tolerance.
Small input impedance (~50Ω) at Master output and Slave inputs helps control edges for non-slew controlled I/O.
  Also improves ESD tolerance.
Level shifting using a series NMOS allows for 3V Master logic while the bus operates at more effective 5V level.
  Bidirectional operation; Note: source connects to Master.
  Adds isolation and protection from direct logic pin exposure.

## Slide 30: Improved Interface
Using V12 to terminate the OneWire bus offers a more constant drive current (1.5-2.5ma) that provides better rise time slope compared to simple 2.2K pullup to 5V.
  Requires some form of clamping, which improves ESD tolerance.
  NOTE: circuit always draws current; excess flows through D1A.
ESD hardened, which protects microcontroller I/O pin (i.e. Raspberry Pi) from damage.
Long pullup tails for simple (2.2K) resistor pullup illustrate need for maximum recovery time between pulses.
Interface can support dozens of devices on single bus.
Sims for 10p, 1500p, and 5000p bus loads (in addition to C1).
SIMPLE 2.2K 5V PU
I/O PIN
BUS IO

## Slide 31: Alternate Interfaces
Circuit A
  Uses a PNP to both clamp the output, at ~5.6V and set a constant pullup current. The optional LED clamps the output at ~3.3+1.7 = 5V. In the high state, the LED sinks excess current and turns on; in the low state it turns off thus indicating a shorted or stuck low bus.
  Sinks excess current into 5V without LED or into 3.3V supply with LED.
  Note: Uses a red LED as other colors may have different voltage drops.
Circuit B
  Uses a PNP pair to make a low dropout current (mirror) source that can operate from a 5V supply and maintain ~4.8V bus level.
  Works from a 5V supply, such as directly from USB.
  Note, resistors R1A and R1B compensate for base voltage differences and allow for a smaller input leg current. They could be omitted when using a matched pair, such as BC857 with R3=2.2K.
Both circuits draw current continuously. The optional enable switch shown in circuit B can be used to disable the current source for lower standby power. Circuit A requires a high-side switch to disable the current.
Many options for constant current as shown.

## Slide 32: DS2413 – 2-bit GPIO DS2408 – 8-bit GPIO
These parts can basically function as remote I/O pins for your design.
  Can be located 1000’ from controller!
  Parasitic powered.
  High voltage (28V) open drain outputs.
Software models treats as a 2/8 bit port.
  reg(): Read/write output register.
  port(): Read from port pins / write to register.
Special switch (state) model as well.
  Operates DS2413 as a 1-bit remote I/O pin actuator (switch) with sensor feedback.
  state(bool): Write sets port bit A to state – OFF/ON. Read gets port pin B for verified feedback.
  DS2408 functions as a 4-pin switch.
  Works for contact sensing too (i.e. read only).

## Slide 33: Ground Loops
When switching remote loads, such as may be attached to a DS2413 at the end of a long bus, some form of isolation (i.e. optical, line receivers, …) must be employed to prevent ground loops which result in the load current returning on the OneWire ground and disrupting bus communications or potentially damaging the controller hardware.
Power and ground must be routed to the loads independently and not sourced from the OneWire bus.

## Slide 34: Old Libraries
Originally used a personally built Perl library that ran under windows.
  Assumed a DS9097 (DS2480B serial port) interface.
  Hard to maintain with constant Perl core charges and Win32 serial support.
  Problems with bus read failures under Windows (serial driver, not Perl) sporadically dropping bytes of data, particularly for operations such as DS18B20 parasitic temperature measurements where bus remains idle for up to a second.
Ported Perl library to Python.
  Used for 10+ years.
  Used under both Linux and Windows – fewer issues than with Perl, but data problems still persistent, particularly with Windows.
OneWire File System
  Dabbled with it, but awkward to use in process control.
  Lot of overhead.
  Sporadic support.
Arduino.
  Poorly defined library really based on the notion that users connect a single DS18B20 sensor to an I/O pin, not at all what OneWire designed for and not well supported for large networks and other device types.
  Unfortunately, most other board developers have copied Arduino design!

## Slide 35: Linux OneWire Kernel Driver
Difficult to use, but it does work – simply put, it’s a mess!
  Raspberry Pi support.
  Poor documentation, particularly for those without kernel experience.
Different inconsistent driver/module for each device type.
  Some devices require root permissions, while other don’t.
  Some types included by default, others not.
  Differences in input/output model across devices.
  Requires understanding complex kernel driver development to add a custom/unsupported device.
  Linux one-off serial number format vs following de facto notation.
Modelled as a file system not as a data agnostic bus like I2C (i.e. simple character device). (Not the most friendly of interfaces for scripts or other tools such as node-red.)
Much better if kernel driver simply supported data agnostic core routines – bus reset and bit read/write (and for efficiency byte/bytearray operations) – then use higher level code such as Python or JavaScript to implement the bus and device specifics.
  Planned rewrite using lgpio library for direct bitbang of I/O pin.
  Beyond my expertise as I don’t program in C.

## Slide 36: Node-red
My most recent system deployments.
  Greenhouse automation.
  Solar hot water system 15 year upgrade.
Raspberry Pi Zero W hardware.
Based on interfacing to Linux kernel driver.
Again limited concept of OneWire.
  OneWire node is really just a DS18B20 interface.
  Rewrite to support DS2413 and DS2408 port interfaces.
    Needs work to release.
    Workaround for root permission.
    More/custom devices needed.

## Slide 37: CircuitPython
onewireio core library well done!
OneWireBus/OneWireDevice libraries, not so much.
  Again limited concept of OneWire functionality.
  Limited device set: only DS18X20 and DS2413.
    DS18X20 does not support parasitic operation and blocks (750ms) while converting temp.
My rewrite of OneWire libraries supports Adafruit devices and more.
  Non-blocking temperature reads by default.
  DS18B20 parasitic operation works.
  More device types and easy custom device extensions.

## Slide 38: QTPy RP2040 Broker
Project to interface a number of sensor types (including OneWire I2C, SPI, and more) to Node-red via the USB interface of the Adafruit QTPy RP2040.
Broker …
  Receives JSON formatted requests from Node-red and (asynchronously) returns JSON formatted responses.
  Relieves RPi or equivalent of the bit management details.
  Makes adding new sensors much easier.
Interface board designed to wrap QTPy with robust interfaces.